Company Name

Quarry Name

Address

City, St Zip

Tele/Fax

Insert Date here	Letter “B”

To: Insert Recipient here

Job: Insert Job here

Aggregates: Rip Rap and Base Coarse Aggregate INDOT 53’s

Insert Company Name here has met all the requirements of the Indiana Department of Transportation to become part of their Certified Aggregate Producer Program (CAPP). It is the responsibility of the Producer to meet the requirements of CAPP. INDOT performs periodic inspections and audits throughout the season to assure compliance with the program.

Insert Company Name here received Insert Source # here and Insert Q# here for our aggregate operation at Insert location here upon meeting the requirements for CAPP in Insert Year here. Since that time CAPP status has been maintained for this source and Q#, and it is still in effect at this time.

The Base Course Aggregate INDOT 53’s and Rip Rap are in the CAPP program. The Insert Source here follows the INDOT Riprap visual specifications:

### Sizes of Riprap

| Gradation Requirements |
| --- |
| Percent Smaller |
| Sizes, mm (in.) | Revetment | Class 1 | Class 2 | Uniform A | Uniform B |
| 750 (30) |  |  | 100 |  |  |
| 600 (24) |  | 100 | 85–100 |  |  |
| 450 (18) | 100 | 85–100 | 60–80 |  |  |
| 300 (12) | 90-100 | 35-50 | 20-40 |  |  |
| 200 (8) |  |  |  | 100 |  |
| 150 (6) | 20-40 | 10-30 | 0-20 | 35-80 | 95-100 |
| 75 (3) | 0-10 | 0-10 | 0-10 |  | 35-80 |
| 25 (1) |  |  |  | 0-20 | 0-20 |
| Depth of Riprap, minimum | 450 mm (18 in.) | 600 mm (24 in.) | 750 mm (30 in.) |  |  |

The Base Course Aggregate INDOT 53’s are a well graded, durable aggregate, with uniform moisture content. Through mechanical measures the base aggregate can be stabilized by compaction. The INDOT  #53 sieve analysis meets the Insert Owner Name here Specified gradation requirements for the No. 2 aggregate in the following table:

| Gradation Requirements |
| --- |
| Sizes (in.) | No. 1 | No. 2 | No. 3 |
| 2 inch | 100 |  |  |
| 1-1/2 inch | 70-100 | 100 |  |
| 1 inch | 45-80 | 60-100 | 100 |
| ½ inch | 30-60 | 30-65 | 40-70 |
| No. 4 | 20-50 | 20-50 | 20-50 |
| No. 10 | 15-40 | 15-40 | 15-40 |
| No. 40 | 5-25 | 5-25 | 5-25 |
| No. 200 | 0-10 | 0-10 | 0-10 |

The Rip Rap and the Base Course aggregate INDOT 53’s are tested and approved Insert frequency here by the Indiana Department of Transportation.

Independent Laboratory test results, Sieve Analysis, and the INDOT Quality Analysis are available upon request.

Sincerely,

Insert Your Name Here

Insert Your Title Here

Insert Company Name Here

Insert Your Phone # Here